SOEM (Simple Open EtherCAT Master)
Slaveinfo
Starting slaveinfo
ec_init on enx3c18a0098715 succeeded.
1 slaves found and configured.
Calculated workcounter 3
Not all slaves reached safe operational state.
Slave 1 State=12 StatusCode= 25 : Invalid output mapping

Slave:1
 Name:ECR60
 Output size: 64bits
 Input size: 112bits
 State: 18
 Delay: 0[ns]
 Has DC: 1
 DCParentport:0
 Activeports:1.0.0.0
 Configured address: 1001
 Man: 00000a88 ID: 0a880001 Rev: 00000200
 SM0 A:1000 L: 128 F:00010026 Type:1
 SM1 A:1080 L: 128 F:00010022 Type:2
 SM2 A:1100 L: 8 F:00010064 Type:3
 SM3 A:1400 L: 14 F:00010020 Type:4
 FMMU0 Ls:00000000 Ll: 8 Lsb:0 Leb:7 Ps:1100 Psb:0 Ty:02 Act:01
 FMMU1 Ls:00000008 Ll: 14 Lsb:0 Leb:7 Ps:1400 Psb:0 Ty:01 Act:01
 FMMUfunc 0:3 1:1 2:2 3:0
 MBX length wr: 128 rd: 128 MBX protocols : 04
 CoE details: 0d FoE details: 00 EoE details: 00 SoE details: 00
 Ebus current: 0[mA]
 only LRD/LWR:0
PDO mapping according to CoE :
  SM2 outputs
     addr b index: sub bitl data_type name
  [0x0000.0] 0x6040:0x00 0x10 UNSIGNED16 Control Word
  [0x0002.0] 0x607A:0x00 0x20 INTEGER32 Target Position
  [0x0006.0] 0x6060:0x00 0x08 INTEGER8 Modes of Operation
  [0x0007.0] 0x0000:0x00 0x08
  [0x0008.0] 0x0000:0x00 0x00
  [0x0008.0] 0x0000:0x00 0x00
  [0x0008.0] 0x0000:0x00 0x00
  [0x0008.0] 0x0000:0x00 0x00
  [0x0008.0] 0x0000:0x00 0x00
  [0x0008.0] 0x0000:0x00 0x00
  [0x0008.0] 0x0000:0x00 0x00
  [0x0008.0] 0x0000:0x00 0x00
  SM3 inputs
     addr b index: sub bitl data_type name
  [0x0008.0] 0x603F:0x00 0x10 UNSIGNED16 Error Code
  [0x000A.0] 0x6041:0x00 0x10 UNSIGNED16 Status Word
  [0x000C.0] 0x6064:0x00 0x20 INTEGER32 Position Actual Value
  [0x0010.0] 0x60FD:0x00 0x20 UNSIGNED32 Digital Inputs
  [0x0014.0] 0x6061:0x00 0x08 INTEGER8 Modes of Operation Display
  [0x0015.0] 0x0000:0x00 0x08
  [0x0016.0] 0x0000:0x00 0x00
  [0x0016.0] 0x0000:0x00 0x00
  [0x0016.0] 0x0000:0x00 0x00
  [0x0016.0] 0x0000:0x00 0x00
  [0x0016.0] 0x0000:0x00 0x00
  [0x0016.0] 0x0000:0x00 0x00
End slaveinfo, close socket
End program